## Slide 1: Extreme discharges of the Rhine and Elbe: Design floods in the future Jaap Kwadijk Director of Science, Deltares Prof. Climate and water management, Twente University

## Slide 2: Who am I
1986 – MSc Quaternary Geology Amsterdam University
1993 – PhD : Effect of Climate change of the discharge of the Rhine, Utrecht University
Since 1997 Delft Hydraulics / Deltares
Currently
  Prof. Modelling climate and water management, TU.Twente
  Chair Scientific board Deltares
Floods: Netherlands, Hong Kong, Egypt, Iran, Mongolia, Surinam

## Slide 3: The Netherlands
2/3 flood-prone,
9 million inhabitants,
65% GNP,
€ 1800 B invested value

## Slide 4: Dutch perspective: water management system are completely regulated
Notes: We can manage nature
Strong believe in models
Strong believe in research

## Slide 5
Perpectives in views and management styles
Based on Cultural Theory
The Dutch
Notes: Werkgevers organisatie Ulrich Grillo, Präsident des Bundesverbands der Deutschen Industrie (Individualist)
Katrin Dagmar Göring-Eckardt vorsitzende Grunen (Egalitarian)
Angela Markl (??) Hierarchist

## Slide 6: Interest is in very rare flood events
Maximum water depths
Efficient flood standards

## Slide 7: The trend is towards more rare events
x
Climate change and subsidence of soil
Flood probability increases
Growth of
population and wealth
Damage by flooding increases
Expected damage increases

## Slide 8: Many urban areas under-protected against floods
Hallegatte et al,
Nature CC 2013

## Slide 9: “Top 20,” today, in terms of population
Courtesy, Jeroen Aerts

## Slide 10: “Top 20,” today, in terms of assets
Courtesy, Jeroen Aerts

## Slide 11
What determines growth in risk?
Hirabayashi et al. (2013): Large growth in risk in S-E Asia due to climate change; (Nature CC)
Winsemius et al. 2015: Confirms the above, but climate change impact is dwarfed by the disproportionate growth of economy in flood prone zones. Nature CC, december 2015)

## Slide 12: Can we detect climate change signals in the Elbe and Rhine (not really)
Annual flows, no floods!)
Courtesy Christoph
Mudersbach
North Sea Region Climate Change Assessment (NOSCCA), in press

## Slide 13: Can we detect climate change signals in the Elbe and Rhine (not really)
Belz JU et al. . Schriftenreihe der KHR, Bd. 1–22. Konlenz und Lelystad
Seasonal flows, no floods!
Courtesy CHR/KHR

## Slide 14: How to solve the quest for info on more extreme events
Extrapolate your observed floods
Use others’ floods
Create your own virtual flood

## Slide 15
Extrapolate your observed floods

## Slide 16
Discharges
Rhine
Elbe
Find a long time series of river flows
Identify annual flow maxima
Order them from low->high
Fit an Extreme Value function through the points

## Slide 18: Oder before and after 1997 flood

## Slide 19: Some difficulties, larger floods may behave unexpectedly

## Slide 20: Can floods become inifitely large?
Can chickens become as big as ostriches???
(they could according to the extrapolation theory)

## Slide 21
Use others’ floods to increase your own knowledge
From: Helmus vd Langemheen (RIZA), Jeanet Onvlee, Gunther Konnen (KNMI), Jaap Schellekens (Deltares)

## Slide 22: Projection of the Elbe 2002 flood on the Rhine basin

## Slide 23
Shift the output of a weather forecast model (HIRLAM)

## Slide 24: Different translation scenario’s
Shift the:
Rainfall pattern 3 degrees towards the west.
Rainfall pattern 4 degrees towards the west.
Rainfall pattern 5 degrees towards the west.and 0.5 degree towards the south
Rainfall pattern 6 degrees towards the west.and 1 degree towards the south
(1 degree E is approximately 68 km; 1 degree S is approximately 100 km)

## Slide 25: Translate rainfall into river flow

## Slide 26: From the hydrologists perspective :
Storage
River flow
Evaporation
Rainfall

## Slide 27: Results

## Slide 28: Result
Rainfall more than 20% higher then during the floods of 1993, 1995 (no 2 an 3 of the 20th century)
But the resulting flow in the Rhine was less then in 1993 and 1995
=> would not lead to flooding in The Netherlands
Why??
The Elbe event happened in summer => rain falls on relatively dry soils (the sponge)
This soil will become more wet, that water will not end up in the river, relatively little water will end up in the river
So lower floods
However: for summer conditions it resulted into an extremely high flood

## Slide 29: Why are the consequences so very different
Mainly difference in protection levels (Netherlands typically 1000 year flood (or even more); Germany 500 year flood (or less)

## Slide 30
Create your own virtual floods
Use weather generators
Use weather prediction products

## Slide 31: Weather generator
Digital maps of daily observed weather Temperature and rainfall
1961-2000
n-year sequence of daily rainfall and temperature patterns
(synthetic series)
statistical analysis of daily autocorrelation (persistence of the weather)

## Slide 32: Time series resampling
Historical precipitation
Simulated precipitation
Rain volume (mm)
0 | 5 | 1 | 20 | 10 | 30 | 10 | 0 | 0 | 0 | … | 
5 | 1 | 0 | 2 | 20 | 10 | 0 | 5 | 30 | 0
5
1
20
10
30
0
0
0
10
0
5 | 1 | 0 | 2 | 20 | 10 | 0 | 5 | 30 | 0
5 | 1 | 0 | 2 | 20 | 10 | 0 | 5 | 30 | 0
5 | 1 | 0 | 2 | 20 | 10 | 0 | 5 | 30 | 0
5 | 1 | 0 | 2 | 20 | 10 | 0 | 5 | 30 | 0
5 | 1 | 0 | 2 | 20 | 10 | 0 | 5 | 30 | 0
5 | 1 | 0 | 2 | 20 | 10 | 0 | 5 | 30 | 0
5 | 1 | 0 | 2 | 20 | 10 | 0 | 5 | 30 | 0
5 | 1 | 0 | 2 | 20 | 10 | 0 | 5 | 30 | 0
5 | 1 | 0 | 2 | 20 | 10 | 0 | 5 | 30 | 0
5 | 1 | 0 | 2 | 20 | 10 | 0 | 5 | 30 | 0
5 | 1 | 0 | 2 | 20 | 10 | 0 | 5 | 30 | 0
Rain volume (mm)

## Slide 33: Time series resampling
Volume (mm)
Largest 4 day sum 45 mm
Largest 4 day sum : 70 mm
0 | 5 | 1 | 20 | 10 | 30 | 10 | 0 | 0 | 0 | … | 
5 | 1 | 0 | 2 | 20 | 10 | 0 | 5 | 30 | 0
0 | 5 | 1 | 20 | 10 | 30 | 10 | 0 | 0 | 0 | … | 
5 | 1 | 0 | 2 | 20 | 10 | 0 | 5 | 30 | 0
Simulated precipitation
Historical precipitation

## Slide 35: Result: estimation of very extreme discharges

## Slide 36: Use products of the weather prediction models

## Slide 37: 2x per day 50 equally possible weather maps

## Slide 38: => From this 50 rainfall and temperature predictions

## Slide 39: From this also 50 possible river flows

## Slide 40: Around each annual maximum flood 50 additional possible floods (example 1993) => more info

## Slide 41: Advantage: we can show what the weather is that leads to such extreme events

## Slide 42: In a nutshell
The interest will focus to the protection to increasingly rare flood events
Extrapolation methods are of limited value for preparing and design, they do not increase understanding
Weather-discharge-flood generators provide more accurate information about return periods of very extreme floods, increase the understanding
Additionally ensemble weather predictions can provide understandable information since a weather anchor man/woman can tell us about the weather that will lead to such events, also increase our understanding
But… I do not understand the characteristics and consequences of 100,000 years flood these remain beyond my imagination (are the natural sciences able to achieve this??)